## Slide 1
On-the-Job Training: Organized by SENSWAT, Engineering Faculty, Kasetsart University
Date: 16 - 17 January 2025
  Fundamental to GIS
  Map making
  Preparing Gridded Gauged Rainfall (GGR) Using IDS
    Data preparation (add points from excel file)
    Creating GGR using Inverse Distance Square (IDS)
  Zonal Rainfall Raster
Project: 30-Year Historical Gridded Rainfall by the Corrective Remote Sensing Product Method in Nam Theun 1 Hydropower Project Watershed
GIS Training

## Slide 2
Geographic Information System (GIS)
GIS is a technology that is used to create, manage, analyze, and map all types of data.
  Data management
    GIS is a foundational system of record. You can store and integrate information from business systems and authoritative sources, magnifying data’s usefulness.
  Mapping and visualization
    From digital maps and dashboards to satellite imagery, 3D, and real time-GIS brings data to life, helping us understand problems and solve them.
  Spatial analysis
    Most data has a location component—everything happens somewhere. With spatial analysis tools, we find hidden relationships and generate new insights from data.
  Communication
    Maps and dashboards communicate complex ideas quickly. Science and data build common understanding, supporting collaboration and problem-solving.
Ref: https://www.esri.com/en-us/what-is-gis/overview

## Slide 3
Fundamental to GIS
Creating a New Shapefile
1. Open GIS Software
  Launch GIS software such as ArcGIS
ArcMap 10.5

## Slide 4
Fundamental to GIS
2. Navigate to Layer Creation
Go to the menu bar and select Layer > Create Layer > New Shapefile Layer.
First Window
Create Project
Open Existing Projects

## Slide 5
Fundamental to GIS
Remark: first time after installing ArcGIS

## Slide 6
Fundamental to GIS
Icon or Command Button , Which has a group of important commands:
Zoom in the map by defining the desired area.
Zoom out the map by defining the desired area.
Use the mouse to move the map to the desired location.
Zoom in the map to fill the entire view window.
Zoom in the map from the screen one level at a time.
Zoom out the map from the screen one level at a time.
Use to return to the previous image.
Use to display the next image.
Use to select features data.
Cancel the area where the boundary has been drawn.
Use the mouse to select location of object in the map
Use to view descriptions of themes displayed.
Use to find the desired information.
Setting the coordinates that show the location on the map.
Use to measure distances on the map. The measurement is displayed in 2 parts:
Segment Length is the length of the last point drawn to the last point to be measured.
Length is the length of entire lines drawn in that distance measurement.
Use to link map data with other data such as script, image data and descriptive data.
Menu Bar is the main menu that controls the operation of the project.
Button Bar is the section below Menu Bar, It is a button that provides quick access to various commands.
Tools Bar is the section below Button Bar that contains various images for ease of use. The contents of the Tools Bar change depending on what is in the active View window. To know what a button does, point to the tool with the arrow and a short description will appear below.

## Slide 7
Fundamental to GIS
Table of content
Add Data
Search
ArcToolbox

## Slide 8
Map making
1. Add data
SHP_Nam_Theun.shp = Shape Nam Theun
SHP_Nam_Theun_Sub.shp = Shape Sub-basin (NT1, NT2, NG, THB)
Rainfall_Station.shp = 34 rainfall stations
Main_river.shp = Main river
Hydro_Arc.shp = Tributary river

## Slide 9
Map making
1. Add data

## Slide 10
Map making
2. Change symbol

## Slide 11
Map making
2. Change symbol: Categories
Right click
1
2
1
2
3

## Slide 12
Map making
2. Change symbol: Categories
Double click

## Slide 13
Map making
3. Label features
Right click
1
3
2
4
5

## Slide 14
Map making
3. Label features
Right click
1
2

## Slide 15
Map making
3. Label features
Double click

## Slide 16
Map making
3. Label features
1
2
3
1
2

## Slide 17
Map making
4. Data frame

## Slide 18
Map making
4. Data frame

## Slide 19
Map making
4. Data frame
1. Right click
2.
3.
1. Right click
2.

## Slide 20
Map making
4. Data frame
Data Frame
Title
Text
Dynamic
Neatline
Legend
North Arrow
Scale Bar
Scale Text
Picture
Oblect

## Slide 21
Map making
4. Data frame
1. Right click
2.

## Slide 22
Map making
4. Data frame

## Slide 23
Map making
5. Add base map

## Slide 24
Map making
5. Add base map

## Slide 25
Map making
6. Export Data

## Slide 26
Map making
6. Export Data

## Slide 27
  Preparing Gridded Gauged Rainfall (GGR) Using IDS
Data preparation (add points from excel file)
Creating GGR using Inverse Distance Square (IDS)

## Slide 28
  IDS
Step 1 : Data preparation
Excel file in “.xls” format
  Station Name UTM/Decimal Degree Coordinates
  Rainfall Data
Shapefile
  Nam Theun Catchment
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 29
Set the Geometry Type
Point: For specific locations e.g., monitoring stations
Line: For linear features e.g., roads or rivers
Polygon: For area features e.g., land parcels
1
2
3
4
Go to the menu bar and (1) Add Data > (2) Connect to folder > (3)Selected folder > (4) Click OK.
  IDS
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 30
5
6
7
8
(5) Selected excel file (.xls) > (6) click Add > (7) Selected sheet > (8) click Add
  IDS
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 31
Define the Coordinate Reference System (CRS)
9
10
11
12
13
14
  IDS
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 32
Save the Shapefile: Name your shapefile (.shp) and save it to a specified directory.
15
16
17
  IDS
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 33
18
19
20
  IDS
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 34
Result
  IDS
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 35
Step 2: Creating GGR using Inverse Distance Square (IDS)
Method 1
Method 2
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 36
How to open Attribute
Step 2: Creating GGR using Inverse Distance Square (IDS)
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 37
Step 2: Creating GGR using Inverse Distance Square (IDS)
  Preparing Gridded Gauged Rainfall (GGR) Using IDS
Shapefile name
Shapefile header
Raster directory
Cell size
2
1

## Slide 38
Step 2: Creating GGR using Inverse Distance Square (IDS)
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 39
Layer properties: Symbology
1
2
3
4
Step 2: Creating GGR using Inverse Distance Square (IDS)
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 40
Example for Classification by Defined Interval
Step 2: Creating GGR using Inverse Distance Square (IDS)
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 41
How to change color?
Method 2
Method 1
Click here
Click here
Step 2: Creating GGR using Inverse Distance Square (IDS)
  Preparing Gridded Gauged Rainfall (GGR) Using IDS

## Slide 42
  Zonal Rainfall Raster
Zonal GGR
Method 1
Method 2

## Slide 43
2
1
  Zonal Rainfall Raster

## Slide 44
Display value
  Zonal Rainfall Raster

## Slide 45
Rainfall time series at 34 stations
Add Raster
Method 1
Method 2
  Zonal Rainfall Raster

## Slide 46
Before
After
  Zonal Rainfall Raster
Rainfall time series at 34 stations

## Slide 47
Zonal Rainfall Raster – Using python code (V2)
  Zonal Rainfall Raster
Python code for zonal statistic
Macro file for read time series data

## Slide 48
  Zonal Rainfall Raster
Zonal Rainfall Raster – Using python code (V2)
Folder for “.tif” file
(CHIRP_BC from project)
Folder for collect data from python

## Slide 49
  Zonal Rainfall Raster
Import module
Check spatial
Create environments
Processing
Define Date (Start - End)
Define boundary and file directory

## Slide 50
  Zonal Rainfall Raster
Click “Run” / “F5”

## Slide 51
  Zonal Rainfall Raster
Zonal Rainfall Raster – Using python code (V2)
Folder for collect data from python
1. Search “ *.dbf ”
2. Click “Name” for sorting

## Slide 52
  Zonal Rainfall Raster
Example output file

## Slide 53
  Zonal Rainfall Raster
Zonal Rainfall Raster – Using python code (V2)
1. Ctrl + A (select all)
2. Shift + Right click
3. Click “Copy as path”

## Slide 54
  Zonal Rainfall Raster
Macro file
Define parameter from
Station Start = ………..
Run Start = ………..
Round = ………
Station Stop = ……….
Run Stop = ……….
from slide 52

## Slide 55
  Zonal Rainfall Raster
Macro file
From slide 53
(Paste path of file)

## Slide 56
  Zonal Rainfall Raster
Macro file

## Slide 57
  Zonal Rainfall Raster
Sheet: Result
Time series data